- Take off and neatly fold cover.

- Make sure the microscope is in its starting position with the stage all the way down, lowest objective lens in place and stage clips spread.

- Unwrap the cord and plug in.

- Place slide on stage.

- Attach stage clips.

- Turn on light.

- Place eye on eyepiece.

- Turn coarse adjustment knob slowly until image comes into focus.

- Turn fine adjustment knob until image is perfectly focused.

- View.

- Experiment with light level by adjusting diaphragm.

- Turn nosepiece so next higher objective lens clicks into place.

- Turn fine adjustment knob until image is perfectly focused.

- View.

- Turn nosepiece so next higher objective lens clicks into place.

- Turn fine adjustment knob until image is perfectly focused.

- Complete viewing.

- Turn nosepiece so lowest magnification objective lens clicks into place.

- Turn off light.

- Unplug.

- Roll stage all the way down.

- Remove and return slide.

- Rewrap cord and make sure microscope is in stating position.

- Replace cover.

# Text boxes

Remember:

¡Never use the coarse adjustment when viewing a slide on medium or high power!